# Table 4.5

# Estimated typical manure characteristics (as-removed)

(derived from ASAE, 2005: Standard D384.2, Manure Production and Characteristics)

|  | Moisture | Total solids | Volatile solids | TKN | NH3-N | P | K | Ca | Na | Zn | Mn | Cu | Mass |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Description | (percent) | (percent) | (% of TS) | Percent (wet basis) | ppm (wet basis) | (kg/hd/d) |
| Beef |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Earthen lot | 33 | 67 | 30 | 1.18 | 0.10 | 0.50 | 1.25 | 1.21 | 3,012 | 85 | 393 | 14 | 7.5 |
| Poultry |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Leghorn pullets | 65 | 40 |  | 2.13 | 0.85 | 1.00 | 1.10 | 1.49 |  |  |  |  | No data |
| Leghorn hen | 59 | 40 |  | 1.85 | 0.88 | 1.21 | 1.31 | 6.40 |  |  |  |  | 0.03 |
| Broiler litter | 31 | 70 | 70 | 3.73 | 0.75 | 0.60 | 1.37 | 1.82 |  |  |  |  | 0.02 |
| Turkey litter | 30 |  |  | 2.18 |  | 0.33 | 1.23 | 5.00 |  |  |  |  | 0.11 |
| Dairy |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Scraped earthen lots | 54 | 46 |  | 0.70 |  | 0.25 | 0.67 | 0.45 | 311 | 1.2 | 1.4 | 0.2 | 35 |
| Scraped concrete lots | 72 | 25 |  | 0.53 |  | 0.13 | 0.40 | 0.31 | 32 | 0.4 | 0.7 | 0.1 | 40 |
| Lagoon effluent | 98 | 2 | 52 | 0.073 | 0.08 | 0.016 | 0.11 | 0.04 | 7 | 0.9 | 1.4 | 2 | 106 |
| Slurry (liquid) | 92 | 8 | 66 | 0.30 | 0.14 | 0.13 | 0.40 | 0.40 | 905 | 25 | 40 | 75 | 67 |
| Equine |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Solid manure | 43 | 65 | 26 | 0.76 |  | 0.24 | 0.99 | 1.13 |  | 51.7 | 135 | 12.70 | * |
| Swine |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Finisher-slurry wet-dry feeders | 91 | 9 |  | 0.70 | 0.50 | 0.21 | 0.24 | 0.25 | 380 | 85.0 |  | 50 | 3-4 |
| Slurry storage-dry feeders | 94 | 6 |  | 0.47 | 0.34 | 0.18 | 0.24 | 0.25 | 380 | 68 |  | 30 | 4.5 |
| Flush building | 98 | 2 |  | 0.20 | 0.14 | 0.07 | 0.17 | 0.04 | 300 | 33.6 | 14.4 | 31.2 | 16 |
| Agitated solids & water | 98 | 2 |  | 0.10 | 0.05 | 0.06 | 0.06 | 0.08 | 215 | 44.4 | 15.6 | 19.2 |  |
| Lagoon surface water | 99.6 | 0.40 |  | 0.06 | 0.04 | 0.02 | 0.07 | 0.01 | 215 | 3.6 | 1.2 | 2.4 |  |
| Lagoon sludge | 90 | 10 |  | 0.26 | 0.07 | 0.25 | 0.07 | 0.04 | 191 | 22 | 80 | 90 |  |

*32.2 kg per head per day for residential, 46 kg per head per day for commercial

Source:  "Source Water Protection for Concentrated Animal Feeding Operations: A Guide for Drinking Water Utilities"; Gullick et al., ©AwwaRF 2006